## Slide 1
MINI PROJECT II · GROUP 20
EcoMesh
Distributed Peer-to-Peer Disaster Relief Communication Mesh
PHASE III — ROUTING, RELIABILITY & SECURITY
TEAM
Miti Shah · Twissha Shah · Tanvi Sheth
GUIDE
Prof. Anuj Tawari

## Slide 2
02 · RECAP
From discovery to a routable, trustworthy mesh
ECOMESH / GROUP 20
02 / 12
Phase II proved two nodes could discover each other and relay a single hop. Phase III turns that into a real mesh — many hops, the best path, nothing lost, nothing readable by a stranger.
WHAT PHASE II LEFT OFF
Nodes could discover direct neighbours only.
A message could be relayed, but only one hop.
No weighting — every link treated as equally good.
No encryption, no signing, no persistent log.
WHAT PHASE III ADDS
Network-wide routing — every node learns the full graph.
Weighted paths — reliability beats hop count.
Reliable delivery — priority, retry, store-and-forward.
Security — end-to-end encryption and signing.
Persistent logging — every message and event, queryable.

## Slide 3
03 · SCOPE
Phase III at a glance
ECOMESH / GROUP 20
03 / 12
01
ADAPTIVE ROUTING
Link-state gossip,
re-flooded network-wide
Weighted Dijkstra over
measured link quality
02
RELIABILITY
Priority queue, duplicate
suppression
ACK + retry, bounded
store-and-forward
03
SECURITY
AES-256-GCM payload
encryption
Ed25519 header signing,
key distribution
04
STORAGE
SQLite (WAL) message
and event log
Every send, forward,
drop, retry — queryable

## Slide 4
04 · ENGINEERING
Four bugs that would have failed silently
Found by writing the tests, not by guessing — each one is now a regression test.
ECOMESH / GROUP 20
04 / 12
GRAPH STUCK AT TWO HOPS
Link-state reports weren't re-flooded past the first neighbour — a node could never learn a route beyond 2 hops. Fixed with origin + sequence numbers so reports propagate network-wide and stale replays are rejected.
FAILURES NEVER PENALISED
The retry logic never told routing.py about a timed-out link — the cost function's failure term was always zero. Now every ACK timeout updates the link's cost immediately, not on the next gossip cycle.
RETENTION QUEUE UNBOUNDED
Store-and-forward had no size or age limit. Now it evicts the lowest-priority message first (SOS is never displaced) and expires anything held past 30 minutes.
SIGNATURES WOULD BREAK AT HOP 1
The spec says “sign header + path” — but ttl, hop_count and path all change at every relay. Signing them would make every signature invalid after one hop. Fixed by signing only the fields that never change in transit.

## Slide 5
05 · ALGORITHM · ROUTING
A longer path can be the better path
ECOMESH / GROUP 20
05 / 12
WEIGHTED LINK COST
cost(u,v) = H + α × (1 − quality) + β × failures
WORKED COMPARISON
PATH | COST | DECISION | STATUS
2 hops · poor links | 7.75 | REJECT | —
3 hops · good links | 3.75 | CHOOSE | ✓ tested
Dijkstra over the weighted graph · O((V+E) log V). Proven directly by an automated test: a two-hop path through unreliable links is rejected in favour of a three-hop path through good ones — the headline claim of the whole routing design, not just a formula on a slide.

## Slide 6
06 · ALGORITHM · PRIORITY
SOS moves to the front — at every hop
Binary min-heap · ordered by (priority, creation time)
ECOMESH / GROUP 20
06 / 12
NORMAL
1
STATUS
2
NORMAL
1
→
SOS
0
SELECTED NEXT: SOS — even though it arrived last
Priority is re-applied at every hop, not just at the source — an SOS queued behind NORMAL traffic at a busy relay still jumps to the front there too.
O(log n) enqueue/dequeue. Proven with a test: a NORMAL packet queued first, an SOS queued second — the SOS is still the one sent first.

## Slide 7
07 · ALGORITHM · SECURITY
Strangers relay it. They still can't read it.
ECOMESH / GROUP 20
07 / 12
CONFIDENTIALITY
AES-256-GCM payload encryption, end to end.
A relay forwards the ciphertext untouched — it never
calls decrypt, by construction.
Proven directly: a relay node configured with no key
at all still forwards correctly — and its own log never
records a plaintext body for a message it only relayed.
AUTHENTICITY
Ed25519 header signing. Public keys travel in HELLO,
then propagate network-wide through the same
re-flooding mechanism as routing — a destination three
hops from the sender can still verify it.
The fix: sign only the fields that survive relaying
(not ttl/hop_count/path). Proven with a 3-hop relay
test — the signature verifies correctly at the far end.

## Slide 8
08 · IMPLEMENTATION · PHASE III
Routing and reliability are built
ECOMESH / GROUP 20
08 / 12
routing.py
Link-state gossip with re-flooding · weighted Dijkstra · route caching
Gateway/rescue terminal selection folded directly into route computation
reliability.py
Priority queue (binary min-heap) · duplicate suppression · ACK tracking with bounded retry
Store-and-forward with count + age bounds and priority-protected eviction
node.py (wiring)
Node.send() — real message origination with ACK/retry/store-forward lifecycle
Multi-hop forwarding via route_resolver, role propagation through gossip
Every routing decision — which link, which hop, which path — now comes from measured reliability, not assumption.

## Slide 9
09 · IMPLEMENTATION · PHASE III
Security and storage, wired end to end
ECOMESH / GROUP 20
09 / 12
crypto.py
AES-256-GCM encrypt/decrypt · Ed25519 generate/sign/verify
Vetted library primitives only — nothing implemented from first principles
store.py
SQLite, write-ahead logging · one database file per node
messages, events, peers — every send/recv/forward/drop/retry, queryable
256
automated tests passing
up from 79 at the end of Phase II — routing · reliability · crypto · store · node integration
Every new feature in Phase III shipped with the test that proves it — including the four bugs on slide 4, each caught by a test before it ever reached a demo.

## Slide 10
10 · GIT EVIDENCE
The repository shows the work
git log --graph · git shortlog -sn
ECOMESH / GROUP 20
10 / 12
BRANCH LINEAGE
develop → develop_2 → develop_3
Each phase branches from the last, inheriting
everything — nothing re-typed, nothing lost.
Tagged: v0.1-phase1 · v0.2-phase2 · v0.3-phase3
Conventional Commits throughout — feat(routing):,
fix(reliability):, docs: — readable without opening
a single file.
WHAT TO RUN LIVE
git log --graph --oneline
— the commit history, phase by phase
git shortlog -sn
— commit distribution across the team
python -m pytest -q
— 256 passed, live, not a screenshot

## Slide 11
11 · SUMMARY & NEXT
From a routable mesh to a visible one
ECOMESH / GROUP 20
11 / 12
DONE · PHASES I–III
SRS, six UML diagrams, Design of Algorithms
Protocol, transport, discovery, relay, simulator
Weighted routing, reliability, security, storage —
all wired into Node, 256 tests passing
NEXT · PHASE IV
FastAPI + WebSocket API layer
Node view — SOS button, live delivery status
Rescue dashboard — live topology, SOS queue
Integration across real machines, demo rehearsal

## Slide 12
THANK YOU
Questions?
Miti Shah · Twissha Shah · Tanvi Sheth
EcoMesh · Group 20